## Slide 1
Satellite Design & Integration
Build Session 4
Payload integration and downlink check
Notes: Day 4, Friday 16 October. 12:00-12:45 and 13:45-14:45, 1 h 30 in total. Follows Lecture 4, Payload and the link to the ground.

## Slide 2
Build Session 4 — Payload integration and downlink check
Fitting the antenna
Notes: The deployable dipole and the closed satellite. No code.

## Slide 3
Satellite Set-up -Antenna OBC Connection

## Slide 4
Satellite Set-up -Antenna

## Slide 5
Satellite Set-up -Antenna
To insert the M2.5x6, open manually deploy the antennas!
Once done, close them back with the pins.

## Slide 6
Satellite Set-up -Discussion

## Slide 7
First code on the ground station
Write a code to turn on one LED if the serial monitor is available (send whatever letter to see if it works). If nothing is sent, the LED should stay off.
Write a code to turn on one LED with a CHARACTER ( serial). E.g. If i send ‘A’ the LED turns on. Similarlym try with string as well.

## Slide 8
Over to the ground station
Now, let's shift our focus from the CubeSat to the ground station.
My ground station will serve as the receiver for all your ground station messages, as there is no cryptography involved.
We will explore data transmission by uploading code exclusively to the ground station.

## Slide 9
Sending a first message over LoRa
Find the appropriate LoRa example (File > Examples > LoRa) for transmitting and open it.
Always use the LoRa.println() function to send messages to the receiving ground station.
In the example you will find a counter, remove it so that you send only one message (one every 5 seconds) -stick to this delay time.
The correct frequency is 434E6.
Send to my GS a message! Keep it short!

## Slide 10
Checking the range of the link
Now, keep the Arduino connected to your ground station. Take your PC, divide your team, with some members staying inside the room and others going outside to move around the area, checking the range of communication. Use your smartphone to call your teammates and determine exactly when the communication stops. Ensure that the message you send includes your identification.

## Slide 11
Sending a message on command
The code from the previous exercise continuously sends the uploaded message on Arduino. Find a way to input a message in the serial monitor (using Serial.read) and ensure it is sent only once. If possible try to send the message with timestamp along with it. (Time stamp optional)
The output should look like: [0m 30s] your_message

## Slide 12
Transmitting the OBC temperature
Now, let's configure the LoRa sender on the satellite, ensuring that the RBF is plugged
Transmit the temperature from the OBC via radio, along with a brief message to identify yourself.
The output should look like:
[NAME OF GROUP] | TEMPOBC = 20.4
Now, figure out a way to send the temperature when inputting 'TEMPOBC' via serial. Implement the option to send also the time with 'TIME'.
The output should look like:
[NAME OF GROUP] | TEMPOBC = 20.4 | TIME = 0m 34s
OBC ONLY.

## Slide 13
Sending every reading by radio
●
Send tomy ground station all your readings via LoRa separately by typing TEMPOBC, TEMPEPS, TIME, TEMPCOMPARISON and VBAT.
The output should look like:
[Team Name] TEMPEPS = 24.20 deg
[Team Name] VBAT = 3.67 V
if you typed “TEMPEPS” or
if you typed “VBAT” …
●
Now, write a new function called sendAll() that is capable of sending all the readings in one line. This function has to be activated when typing “ALL”.
The output should look like:
[1m 25s][Team Name] TEMPOBC | TEMPEPS = 24.20 deg | VBAT = 3.67 V

## Slide 14
Addtothecodethepossibility of typing “STATUS” to get an output that looks like this:
● ● ●
[3m43s] NOMINAL
[3m43s] WARNING! TEMPxx is too high: 35 deg!
[3m43s] WARNING! VBAT is too low: 3.5 V!
if no warnings are found
if temperature is too high
if battery is too low
Now,inthesendAll() function include the STATUS of the satellite in two lines.
[2m23s][Team Name] TEMPOBC | TEMPEPS = 24.20 deg | VBAT = 3.67 V | [2m23s][Team Name] STATUS = one_of_the_cases_above

## Slide 15
●
When you are done SAVE YOUR SKETCH AS OBC_DAY5!
Implement a code to monitor the STATUS so that, even when we don't explicitly request 'ALL' or 'STATUS,' if the satellite detects a warning, it will send a message to the ground station via LoRa.
[6m 15s] [Team Name] STATUS = WARNING! VBAT is too low: 3.5 V!

## Slide 16
Taking a picture
The satellite has a serial camera module called Adafruit VC0706.
By referring to its online documentation:
will see how to convert it to JPG!
Create a new sketch.
Refer to the OBC schematics to understand the camera connection to Arduino.

## Slide 17
Camera & CoolTerm
To capture a picture with the OBC camera we need to open CoolTerm.
-Code Solutions Day6!

## Slide 18
Final Exercise -Challenge!
Configure your entire satellite so that it takes the following commands from your ground stations!

## Slide 19
Final Exercise Solution
Upload the OBC, ADCS and GS codes into their respective boards from GitHub. Change the password in OBC, ADCS and GS code, matching them, so that only your ground station is configured with your satellite.
Check the code working!

## Slide 20
Satellite Set-up -Full Satellite
Congratulations, you built the entire 1U Cubesat!