## Slide 1: Payload Systems
Lecture 5
1

## Slide 2: Lecture Outline
Satellite Payload, classifying payloads, spacecraft configuration, payload design and selection
Remote sensing: Active and passive sensors
Optical, microwave sensors
Comms payloads
2

## Slide 3: Lecture Objectives
By the end of this lecture, students will be able to:
  Explain the role and functions of satellite payloads.
  Classify payloads according to mission objectives and applications.
  Explain how payload requirements influence spacecraft configuration.
  Identify key payload design and selection criteria.
  Distinguish between active and passive remote-sensing sensors.
  Compare optical and microwave sensors.
  Explain the functions and architecture of communications payloads.
  Select suitable payload technologies for a given mission.
3

## Slide 4: Satellite Payload/Mission Subsystem
Payload is the combination of hardware and software on the spacecraft that interacts with the subject.
Payload is unique to each satellite mission and the main reason that the spacecraft is developed.
Payload is the main driver for mission analysis and design: it is central in the design of the satellite bus system.
4

## Slide 5: Spacecraft Configuration
Spacecraft configuration is an overall arrangement of payload and subsystems inside the spacecraft body as well as an external architecture of the spacecraft
Mars Global Surveyor (1996 – 06), Source: NASA
5

## Slide 6: Payload Design and Configuration
The following are the major payload design drivers:
The payload constitutes a fundamental design driver:
  Number of instruments/equipment
  Their mass, size, power, field of view, data rate, etc.
The payload orbit needs:
  Where to operate? (LEO, GEO, HEO, etc)
  How to get there and remain in desired orbit?
  Where and how accurately to point?
The rest of the spacecraft is really there just to satisfy the payload and mission objectives in terms of:
  Mechanical support
  Thermal control, etc
6

## Slide 7
Derived from User Need
Payload Design Flow
7

## Slide 8
Classifying Payloads
Payloads are described in two different ways: by what the instrument is, and by what the mission uses it for. The two overlap.
BY INSTRUMENT
What the hardware is
Imaging
Visible, multispectral and hyperspectral cameras
Radio
Transceivers, transponders, software-defined radios
Field and particle sensors
Magnetometers, Langmuir probes, radiation detectors
Spectrometers
Analysing the spectrum of emitted or reflected light
Experiment modules
Biology, materials and other hardware under test
BY PURPOSE
What the mission uses it for
Earth observation
Imaging land, ocean, atmosphere and infrastructure
Science
Collecting data against a research question
Communication
Carrying a link for users on the ground or in orbit
Navigation
Position, timing and navigation experiments
Technology demonstration
Proving a component or technique in orbit
The same instrument can be a different payload on a different mission. A camera is an Earth observation payload on one satellite and a scientific instrument on another. A magnetometer is the science payload on one and an attitude sensor on most other CubeSats.
8
Notes: The point of the slide is the band at the foot. What makes a piece of hardware the payload is not what it is, but the role it plays in the mission. The magnetometer example is the clearest: identical part, science instrument on one satellite, attitude sensor on the next.

## Slide 9
Selecting a Payload
Five questions decide which instrument a mission can carry, and every one of them reaches back into the platform.
1
What has to be observed or
delivered
The mission objective, expressed as something measurable. Everything below follows from it (land surface, fire, smoke, vegetation, oceans, clouds, magnetic fields, weather systems)
2
How often, and from where
Revisit rate and orbit. These decide the orbit, and the orbit decides the illumination, the eclipse and the pass duration.
3
What the instrument demands
Pointing stability, aperture, power draw and operating temperature range.
4
How much data it produces
Data volume per observation, against the downlink rate and the time a ground station is in view.
5
Where the processing happens
On board, if the data is small and can be defined before launch. On the ground, if the raw observation must be preserved.
A payload is selected against what the platform, the orbit and the link can support.
Payload Systems
9
Notes: The closing reference slide. Work down the list once. Every question has appeared earlier in the lecture — XI-IV answers the fourth, and the ship-counting example answers the fifth.

## Slide 10: Payload Drivers
Instrument Type | Main Drivers on Spacecraft Design
Hi-Res Visible/IR imager | Data rate (storage, transmission). Pointing and stabilization.
Thermal IR | Detector cooling. Calibration.
SAR | Data rate (storage, transmission) Antenna storage and deployment. Power demand, thermal dissipation. Electromagnetic compatibility (EMC).
Passive microwave | Antenna size.
Altimetry | Precise in-orbit determination.
10

## Slide 11: Payload Design Characteristics
11
Sensor design and sizing are determined by a complex trade-off among
  spatial,
  spectral, and
  Temporal
Each performance measure is improved at the expense of the others.
Developing a design that balances all of these performance parameters while minimizing size, cost, and technical risk is the essence of sensor system engineering.

## Slide 12: Sentinel Satellites
12

## Slide 13: Key Points in Spacecraft Design Review
What are payload characteristics - size, shape, etc?
How to support the payload most efficiently?
What about payload operations - continuous or not?
How is data to be retrieved?
How should we achieve and maintain the desired operating orbit? - significant propulsion implications.
Which AOCS concept is necessary/preferred?
What is the total power and energy demand? - hence solar array area and battery capacity, etc……
Propulsion, AOCS and solar array are often the most significant drivers on (mechanical) configuration
13

## Slide 14: EO & Remote Sensing Sensors
Sensors are sensitive to electromagnetic energy such as:
  Light, heat, radio waves
Active Sensors
  Emit their own source of energy and record the radiation that is reflected or backscattered from the target
Passive Sensors
  Detect natural radiation emitted or reflected by targets
14

## Slide 15: Remote Sensing Sensor Types
15

## Slide 16: Remote Sensing Platforms
Remote sensing Platform | Typical Spatial Resolution | Typical Field-Of-View (FOV)
Satellites | 2 - 15 m | 10 – 50 km
Aircraft (piloted) | 0.2 – 2 m | 2 – 5 km
Miniature UAV | 1 – 20 cm | 50 – 500 m
Ground-based | < 1 cm | < 2 m
Platform is the vehicle carrying the remote sensing device.
16

## Slide 17: Earth Observation & Remote Sensing Payloads
17

## Slide 18: Optical Imaging Sensors
 | Panchromatic | Multispectral | Hyperspectral
Spectral range (nm) | ~ 430 - 720 | ~ 430 – 720 ~ 750 – 950 | ~ 470 - 2000
Satellites | QuickBird, SPOT, IKONOS | QuickBird, SPOT, IKONOS | TRW Lewis, EO- 1
Spectral band | Monospectral, black and white, grey-scale image (1 band) | Several spectral bands (3 – 10 bands) | 10 to 100 spectral bands
Spatial resolution | Submeter | Up to 1- 2 m | Up to 2m
Applications | Earth observation and reconnaissance applications | RGB (True colour): Visual analysis Green Red Infrared: Vegetation and camouflage detection; Blue-NIR-MIR: Visualizing water depth, vegetation coverage, soil moisture content and presence of fire. | Agriculture,mineralogy, surveillance, physics, astronomy.
18

## Slide 19: Reflectance Spectra
19

## Slide 21: Camera Specification
https://www.uctronics.com/https-www-uctronics-com-index-php-arducam-ov2311-mipi-2mp-global-shutter-mono-camera-module-html-2268.html
Specification | Value
Sensor | OV2311 Monochromatic
Camera Resolution | 2MP
FOV | 83º (H)
Ground Swath | 255x203km @ 400km attitude
Ground Resolution | 100m @ 400km attitude
21

## Slide 22: Camera Block Diagram
22

## Slide 23: Camera Hardware
CAM1
CAM2
RasPI zero W
Memory: 512MB RAM
OV2311 Monochromatic
Lens Focal Length = 8mm
Ground Resolution of less than 100m
Ground Swath 255kmx203km @ 400km.
µSD Card
Kingston 64Gb
23

## Slide 24: Mission Modes - CAM
Camera Mode | Required Inputs |  |  | Image Capture | Image Compression? | Store Data to Camera Memory?
 | Camera Pointing to Earth? | Satellite Location needed? | Time required? |  |  | 
Normal | No | No | No | Single Shot | Yes | Yes
Continuous | Yes | No | No | Burst | Yes | Yes
Timed | Yes | No | Yes | Burst | Yes | Yes
24

## Slide 25: Mission Modes - CAM
FLOWCHART
Normal Mode
Continuous Mode
25

## Slide 26: Concept of Operation(Execution)
CAM MCU executes the command received
Take photos – saves images in SD Flash memory.
Image transfer – copies photos to shared FM2.
Main PIC copies data from Shared FM2 to Shared FM1.
Send command from GS.
Antenna receives command.
COMM PIC relays command to Main PIC.
All DIO communications (turn on and off, and trigger) are routed through CPLD.
UART communications (capture, copy and erase) are routed through MB-CPL.
26

## Slide 27: Concept of Operation (Downlink)
Data from Shared FM1 is sent to the ground station.
Data is received by the ground station.
Hex Data is converted to JPEG using FavBinEdit.
Send command from GS.
Antenna receives command.
COM PIC relays command to OBC (Main PIC).
27

## Slide 28: Integration Test summary
PC or GS operation software (cmd) | Passed/Failed | Remarks
2E turn on CAM1 | Passed | CAM was turn on.
2E turn on CAM2 | Passed | CAM was turn on.
Wait for 2 minutes before sending command to RPi |  | 
220028 Initialize CAM1 | Passed | ACK. was received
320038 Initialize CAM2 | Passed | ACK. was received
Wait for 10 seconds before sending trigger |  | 
35 triggers both CAMs | Passed | Capture executed
220029 CAM1 copy thumbnails | Passed | Photos were saved
320039 CAM 2copy thumbnails | Passed | Photo was saved
22002A11 image name 17.jpg for CAM1 | Passed | Photo was saved
32003A14 image name 20.jpg for CAM2 | Passed | Photo was saved
12000000000900 get packets | Passed | HEX. Files downloaded
20 turn off CAM1 | Passed | ACK. was received
30 turn off CAM2 | Passed | ACK. was received
28

## Slide 29: Camera Functional Test
720nm
790nm
550nm
680nm
Water Body
Settlement
Empty Field
29

## Slide 30: Success Levels
Success Levels | Criterion
Minimum | Capture multispectral image of any target on earth with Ground Resolution of < 175m and Swath > 70Km x 70Km. Downlink at least 40 images over mission lifetime Achieve at least half total area mapping of one target member country
Medium | Capture multispectral data of target countries with Ground Resolution of < 175m and Swath > 70Km x 70Km. Downlink at least 80 images over mission lifetime Achieve at least half total area mapping of two target member countries Write paper on performance
Full | Downlink at least 150 images over mission lifetime Achieve full area mapping of all target member countries Write paper on outcomes and achievements.
Extra | Downlink 200 images Share data with interested parties Achieve data mapping for additional countries
30

## Slide 31: LiDAR (Light Detection And Ranging)
Active sensor
Laser radiation is returned (‘backscattered’) from atmospheric particles or by reflection at the Earth’s surface.
Measuring the return pulse delay time and the intensity can be used to investigate Terrain mapping, vegetation analysis, elevation, and atmospheric studies.
31

## Slide 32: Synthetic Aperture Radar (SAR)
Radar emits a series of short, high power pulses of microwave radiation at a fast rate (active illumination).
Pulses travel to the ‘target’ and a small fraction of the emitted radiation is reflected back to the sensor and detected.
The detected signal depends on the backscatter coefficient of the surface, the range, receiver size, etc.
32

## Slide 33: LiDAR, Optical, and SAR
Differences Between LiDAR, Optical Sensor, and SAR (Tsai et al., 2019) (Space Based Infrastructure Monitoring) (National Ecological Observatory Network) (Tshabalala et al., 2020) (WMO Oscar)
(Hu et al., 2017)
33

## Slide 34: Radiometers & Altimeters
Microwave/infrared instruments to measure sea surface height, wave heights, ocean surface temperatures, and polar ice sheet thickness.
Copernicus Imaging Microwave Radiometer, CIMR

## Slide 35: Communication Payloads
35

## Slide 36: Communication Payloads
Designed to receive, process, and retransmit signals across global networks.
Transponders (C, Ku, Ka, Q/V bands): Analog/digital frequency converters and amplifiers used to relay television, radio, internet, and data signals (e.g., Starlink, Eutelsat).
Phased Array / Multi-Beam Antennas: Electronically steerable antennas used for high-throughput internet service and targeting specific ground locations.
Optical Inter-Satellite Links (Lasercom): High-speed laser transceivers for data exchange directly between satellites in orbit without ground relays.

## Slide 37
Mission Background :
Difficulty in gathering data from remote areas
  No need for ground network infrastructure which is costly to establish & maintain.
Data to be used for:
Solar Illumination Measurement/Mapping
Disaster Mitigation
End users:
Energy & power development sectors
Disaster & preparedness ministries
SF-WARD MISSION
https://www.bbc.com/news/world-africa-45836381
37

## Slide 38
Mission Background:
APRS – Automatic Packet Reporting System
DP - Digipeater
APRS Functions in Amateur Radio Service
Emergency Disaster Mitigation
Rescue and Relief operation
Learning & contribution to the Amateur Radio Community
APRS-DP
38

## Slide 39: Navigation & Timing Payloads
39

## Slide 40: Navigation & Timing Payloads
Provide precise time and positioning coordinates across global positioning systems (GPS, Galileo, BeiDou, GLONASS).
Atomic Clocks (Rubidium / Hydrogen Maser): Ultra-precise timing sources required to calculate time-of-flight positioning with nanosecond accuracy.
GNSS Signal Transmitters: Dual-band navigation signal generators transmitting L-band navigation frames.
Rubidium Pulsed Optically Pumped (Rb POP) atomic clock by Leonardo, Italy

## Slide 41: Scientific & Planetary Exploration Payloads
41

## Slide 42: Scientific & Planetary Exploration Payloads
Instruments mounted on space observatories and interplanetary probes to collect astrophysical and planetary data.
Space Telescopes & Mirrors: Optical assemblies for observing distant stars, galaxies, and exoplanets (e.g., James Webb Space Telescope, Hubble).
X-ray & Gamma-ray Spectrometers: Instruments designed to register high-energy photons emitted by black holes, neutron stars, and solar flares (e.g., Chandra X-Ray Observatory).
Magnetometers & Particle Analyzers: Instruments that measure planetary magnetic fields and solar wind interactions (e.g., Europa Clipper, Parker Solar Probe).

## Slide 43: Weather & Environmental Payloads
43

## Slide 44: Weather & Environmental Payloads
Specialized meteorological instruments operating in low Earth orbit (LEO) or geostationary orbit (GEO).
Sounders (Infrared / Microwave): Measure atmospheric temperature profiles and moisture distribution at varying altitudes (e.g., GOES series, MetOp).
Lightning Mappers: High-speed optical detectors that monitor cloud-to-ground and intra-cloud lightning strikes continuously.
GOES geostationary lightning mapper (GLM)
Sounders (Infrared / Microwave)
44

## Slide 45
In-orbit Demonstration
A technology can be flown as the payload, so that its behaviour in the real environment is known.
45
Notes: GreenCube grew microgreens in a 3U above the Van Allen belts. Worth one minute. The wider point for this audience is that demonstration missions have clean, verifiable objectives, which makes them a natural fit for a first mission.

## Slide 46: Satellite as a Platform: Sensors
46

## Slide 47
References and Further Reading
Open sources used in this session. Worth returning to after the course.
NASA State-of-the-Art of Small Spacecraft Technology
Free report, updated regularly. A full chapter on payloads
https://www.nasa.gov/smallsat-institute/sst-soa
MarCO — NASA JPL
The two CubeSats that relayed InSight's landing from Mars
https://www.jpl.nasa.gov/missions/mars-cube-one-marco
ESA Web TV — CubeSats
Mission footage and payload demonstrations, over fifty videos
https://www.esa.int/ESA_Multimedia/Keywords/System/CubeSats/(result_type)/videos
Nanosats Database
Every nanosatellite launched, searchable by payload type
https://www.nanosats.eu/
ESA Technology CubeSats
In-orbit demonstration missions and their results
https://www.esa.int/Enabling_Support/Space_Engineering_Technology/CubeSats
Payload Systems
47
Notes: Every link is a public, maintained source. The NASA State-of-the-Art report is the single most useful reference for anyone continuing this work.

## Slide 48
Exercise 5 — What Comes Down
Fifteen minutes, in your team, on the design sheet.
10 min
THE TASK
1
Work out how much image data you can return to the ground in one day.
2
Work out how much the payload produces in one day if every image is kept.
3
The two numbers do not match. Decide what the onboard AI should discard, and what must always come down whatever happens.
4
Write the one line you would put in front of the customer to justify that decision.
ASSUME FOR THIS TASK
Image size
2 Mbit
Images taken per day
200
Downlink rate
9.6 kbit/s
Passes per day
4
Useful time per pass
8 min
48
Notes: Expected working: 4 passes × 8 minutes × 60 × 9.6 kbit/s ≈ 18.4 Mbit a day, against 200 × 2 = 400 Mbit produced — the link returns under five per cent of what the camera takes. That gap is the whole reason onboard processing exists, and it is the point Φ-sat-1 demonstrated by filtering cloudy images before downlink. The figures here are stated assumptions for the exercise, not kit measurements. The answer that should never be discarded is the housekeeping telemetry: without it the team cannot tell whether the satellite is healthy, and that is the argument to put to the customer.